## Slide 1: How can we quantify resistance?
Ohm’s Law states that the current density inside the conductor is related to the electric field causing the charges to move via
The resistivity is a physical property of the material that makes up the resistor
Using the resistivity, we can define a geometric quantity of the resistor:

## Slide 2
We introduce the resistance, which is dependent on ρ of the material and on the geometry of the resistor
This gives us the familiar form of Ohm’s Law:

## Slide 3: Ohm’s Law
When a voltage difference ∆V is applied across a resistor R, the voltage difference causes electrons to flow through the resistor
This flow of electrons is the electric current I. These quantities are related by Ohm’s Law:
Current convention: the flow of positive charge (opposite the flow of negative charge)
Both define a current I pointing to the right, so it is more convenient to think in terms of + charges moving
+
–

## Slide 4: Ideal wires & batteries
Real wires always have some resistance to them, but it is usually small enough that we can ignore it.
In this class we will usually treat wires as ideal, meaning ∆V = 0 across any wire segment even if there is a current flowing.
A battery is any source that supplies a voltage difference in an electric circuit. The voltage is either specified by V or by the symbol which stands for electromotive force (EMF)
Real batteries also have a resistance to them and we will see later how to account for this.
+ terminal
– terminal

## Slide 5: A Basic Circuit
The simplest circuit has an ideal battery, ideal wires, and a single resistor.
Kirchhoff’s Loop Rule:
The sum of the voltage differences around a closed loop in a circuit must be zero.
(conservation of energy)

## Slide 6: A Basic Circuit
The voltage across a resistor is negative if you are going around the loop in the direction of the flow of current.
Current flows from the negative terminal to the positive terminal
ideal wires
Ohm’s Law

## Slide 7: A Basic Circuit
The voltage across a resistor is positive if you are going around the loop in the opposite direction of the flow of current.
Voltage across a battery is negative going from positive to negative
ideal wires
Same as before

## Slide 8: Resistors in Series
Kirchhoff’s Loop Rule:
Current through each R is same
Rewrite this as
Define an equivalent resistance

## Slide 9: Resistors in Parallel
Loop 1:
Loop 2:
Loop 3:
Loop 1
Loop 2
Loop 3

## Slide 10: Resistors in Parallel
Resistors in parallel: